## Slide 1: Ideal Burn Unit Functional design in limited Resource Countries
Amr MOGHAZY
Professor of Plastic Surgery and Burns
Faculty of Medicine, Suez Canal University,
Ismailia, EGYPT.
.

## Slide 2: Elements
Architectural design.
Functional design.
Infection control:
  Unit;
  Patients’ rooms.
Special considerations:
  Visitors/companions;
  Power supply;
  Cost reduction.

## Slide 3: What is the Burn Unit?
INTERBURN standards classification:
  Level 2:
    Working horse of the Burn Care system.
WHO classification:
  District hospital:
    Detached/Affiliated to it.
Level of care:
  Less than 40% TBSA.

## Slide 4: Architectural design
Preferably separate building:
  Easier to control;
  Possibility of extension;
  Delayed admission???
Last floor:
  Limit access;
  Possible extension.
  Lifts?????

## Slide 5: Architectural design
Separate accesses:
  Patients;
  Staff;
  Visitors.
Separate rooms:
  Single patient per room:
    Even if small.
  Possible doubles:
    For moderate/minor cases only.

## Slide 6: Architectural design
ICU suite:
  Capacious rooms:
    ICU equipment.
Operative suite:
  Nearer to ICU.
Inpatient (ward):
  No dressing room.
Nursing station:
  Central:
    Access to all the unit.

## Slide 7: Architectural design
Outside corridors:
  Two:
    Opposite the ward;
    ICU.
Inside corridor :
  Starting at the patient entry;
  Connecting all the interior suites.

## Slide 8: Architectural design
Lockers’ suite:
  At the end of outside corridor.
  Toilets.
Staff suite:
  Meeting facilities;
    Catering and distraction.
Greenery scenes:
  If possible.

## Slide 9: Architectural design (extras)
Recreation suite:
  Central location;
  Contain appropriate facilities:
    Particularly children:
      Toys and playing aid.
Daylight exposure:
  Preferably in all rooms;
    Recreation suite
    Staff room.

## Slide 10: Architectural Design
Operative Suite
Staff
Lockers
ICU
Suite
Patient Suite
Nursing
Recr
Corridor
Corridor

## Slide 11: Outside Corridors
Dirty:
  No sterilization.
Entrance/Exit:
  Personnel;
    Visitors/companions;
  Supplies;
  Wastes.

## Slide 12: Inside Corridors
Clean:
  Sterile.
Circulation inside the unit:
  Personnel;
    Patients.
Video surveillances.

## Slide 13: Rooms
Two opposing accesses:
Double doors:
  Sealed;
  Electric command.
    Handles from inside:
      Except for the clean corridor.
Toilet included:
  Shower in the room:
    Shower trolley/chair.

## Slide 14: Functional Design

## Slide 15: Unit Infection control
Closed Unit:
  Restricted access to patients.
Visitors are not allowed in the Unit:
  Outside corridor.
No contact between patients:
  Bathing and dressing in the rooms.

## Slide 16: Unit Infection control
Hot water:
  No reservoir heaters:
    Solar heaters.
No waste circulation within the unit.
Double doors for all rooms:
  Limit air from patient to inside corridor:
    Minimizing cross-infection.
No dressing room:
  Shower trolley.

## Slide 17: Room Infection control
Single patient per room:
  Minimizes cross-infection.
Separate air outflow for each room:
  No cross-infection;
  No circulating/persistent organisms.
Laminar air flow in all rooms:
  Continuous patient protection.
Double doors:
  Not to be opened at the same time.

## Slide 18: Low-cost Laminar flow in Rooms

## Slide 19: Special considerations
Limited resources:
  Avoidance of sophistications.
Power supply instability:
  Solar energy:
    Water heating.
Water supply:
  Clean running water assured:
    Local water station??
      Solar energy.

## Slide 20: Avoidance of sophistications

## Slide 21: Visitors
Huge problems in most settings:
  Uncontrollable;
  Infection source.
Might be a psychological burden:
  Patients;
  Personnel.
Should be controlled:
  Limited time/number of visits/visitors;
  Limit access to unit facilities.

## Slide 22: Companions
Might be problematic:
  Uncooperative;
  Exhaust staff and resources.
Could be beneficial:
  Help in care;
  Psychological support to the patient.
Should be educated:
  Patients surveillance;
  Infection control procedures.

## Slide 23: Conclusion
Developing countries:
  Should develop code for their Burn Units:
  Adapted to their resources;
  Addressing their particular needs.
Outside corridors:
  Effective in infection control.
Single rooms should be the rules:
  ICU;
  Major cases.

## Slide 24: Conclusion
Simple things could be effective:
  If the objective is understood.
Outflow of air is crucial in rooms:
  Avoid bacterial resistance:
    Abolish cross-infection;
    Avoid permanent organisms.
Companions might be valuable:
  Overcome nursing lack;
  Potential workers in the Burn field.

## Slide 25: Amr Moghazy moghazy@yahoo.com
Thank you!